## Slide 1
COMP.2030 Computer Organization
& Assembly Language
Blackboard
  Syllabus
  Class notes
  Homework/programming assignment

## Slide 2
Textbook and Outline
Textbook
  Randal Bryant and David O’Hallaron
    “Computer System: A Programmer’s Perspective,” 3rd ed. Prentice-Hall
    http://csapp.cs.cmu.edu/public/students.html
Outline in roughly four parts
  Chaps 2 – Data format
  MIPS Assembly Language
  Chap 3 – IA 64
  Chap. 4 -- Hardware

## Slide 3
Course Theme
2030 Computer Org. & Assembly Lang. is required course
  Is a knowledge of computer organization and underlying hardware required for software engineers ?
  But, is this useful to proficient programmers ?

## Slide 4
Course Theme
Bad News
  Hardware or low-level is ugly
    Many details
    Can be counter-intuitive
Good News
  Do not need all low-level technical details
  Sufficient with just enough details

## Slide 5
Course Theme
Good programmers understand how programs affect underlying hardware
  instructions
  Memory access
  I/O and timing
Good programmers understand how programs are affected by underlying hardware
  How to avoid hardware limitation
  Write programs that are faster, smaller, less prone to errors

## Slide 6
Course Theme
Courses so far emphasized abstraction
  Abstract data types
  Asymptotic analysis
These abstractions have limits
  Especially in the presence of bugs
  Need to understand underlying implementations
Useful outcomes
  Become more effective programmers
    Able to find and eliminate bugs efficiently
    Able to tune program performance
  Prepare for later “systems” classes in CS & ECE
    Compilers, Operating Systems, Networks, Computer Architecture, Embedded Systems
Abstraction is good, but don’t forget reality!

## Slide 7
Reality #1
Int’s are not Integers, Float’s are not Reals
Examples
  Is x2 ≥ 0?
    Float’s: Yes!
    Int’s:
      40000 * 40000 --> 1600000000
      600000 * 600000 --> ??
  Is (x + y) + z = x + (y + z)?
    Unsigned & Signed Int’s: Yes!
    Float’s:
      (1e20 + -1e20) + 3.14 --> 3.14
      1e20 + (-1e20 + 3.14) --> ??

## Slide 8
Computer Arithmetic
Does not generate random values
  Arithmetic operations have important mathematical properties
Cannot assume “usual” properties
  Due to finiteness of representations
  Integer operations satisfy “ring” properties
    Commutativity, associativity, distributivity
  Floating point operations satisfy “ordering” properties
    Monotonicity, values of signs
Observation
  Need to understand which abstractions apply in which contexts
  Important issues for compiler writers and serious application programmers

## Slide 9
Reality #2
You’ve got to know assembly
Chances are, you’ll never write program in assembly
  Compilers are much better & more patient than you are
Understanding assembly is the key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language model breaks down
  Tuning program performance
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state

## Slide 10
Reality #3
Memory Matters
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 11
Memory Referencing Bug Example
main ()
{
long int a[2];
double d = 3.14;
a[2] = 1073741824; /* Out of bounds reference */
printf("d = %.15g\n", d);
exit(0);
}
Alpha
MIPS
Linux
-g
5.30498947741318e-315
3.1399998664856
3.14
-O
3.14
3.14
3.14
(Linux version gives correct result, but implementing as separate function gives segmentation fault.)

## Slide 12
Memory Performance Example
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
21 times slower (Pentium 4)

## Slide 13
The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
2.67 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache

## Slide 14
Memory Performance Example
Implementations of Matrix Multiplication
  Multiple ways to nest loops
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}

## Slide 15
0
20
40
60
80
100
120
140
160
matrix size (n)
ijk
ikj
jik
jki
kij
kji
Matmult Performance (Alpha 21164)
Too big for L1 Cache
Too big for L2 Cache

## Slide 16
Compilation System
#include <stdio.h>
Int main()
{
printf(“hello, world\n”);
}
Hello program
  Compile
    gcc –o hello hello.c

## Slide 17
Pre-
processor
(cpp)
hello.i
Compiler
(cc1)
hello.s
Assembler
(as)
hello.o
Linker
(ld)
hello
hello.c
Source
program
(text)
Modified
source
program
(text)
Assembly
program
(text)
Relocatable
object
programs
(binary)
Executable
object
program
(binary)
printf.o

## Slide 18
Assembly Example
Compute the class average
total = 0
counter = 0
while grades[counter] >=0:
total = total + grades[counter]
counter = counter+1
if counter > 0:
average = total/counter
print average
else:
print 'no grades were entered'

## Slide 19
total = 0
counter = 0
while grades[counter] >=0:
total = total + grades[counter]
counter = counter+1
if counter > 0:
average = total/counter
print average
else:
print 'no grades were entered'
Reg1 = 0
Reg2 = 0
Rept:
If (grades[Reg2]<0) goto Sum_done
Add Reg1, Reg1, grades[Reg2]
Add Reg2, 1, Reg2
goto Rept
Sum_done:
if (counter <= 0) goto Done
average = Reg1/Reg2
print average
goto Exit
Done:
print 'no grades were entered'
Exit:

## Slide 20
Reg1 = 0
Reg2 = 0
Rept: Reg3 = grades[Reg2]
Compare(Reg3, 0)
Branch(LT) to Sum_done
Add Reg1, Reg1, Reg[3]
Add Reg2, 1, Reg2
goto Rept
Sum_done:
Compare(Reg2,0)
Branch(LE) to Done
Reg3 = Reg1/Reg2
print Reg3
goto Exit
Done:
print 'no grades were entered'
Exit:
Reg1 = 0
Reg2 = 0
Rept:
If (grades[Reg2]<0) goto Sum_done
Add Reg1, Reg1, grades[Reg2]
Add Reg2, 1, Reg2
goto Rept
Sum_done:
if (counter <= 0) goto Done
average = Reg1/Reg2
print average
goto Exit
Done:
print 'no grades were entered’
Exit: