## Slide 1: 4.2 Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 2: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 3
Combinational logic
  No memory
  A set of inputs uniquely and unambiguously specifies what outputs are
  Defined by a truth table
  e.g. Inputs – A,B,C; Outputs – D,E,F
  Design Process: collect input combinations producing ones in the output
4.2. Logic Design

## Slide 4
    D = A+B+C
    F = A^B^C
    E = A’BC + AB’C + ABC’ => canonical form
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1
Truth Table

## Slide 5: Bit Equality
  Generate 1 if a and b are equal
Bit equal
a
b
eq
eq = (a&&b)||(!a&&!b)

## Slide 6: Word Equality
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 7: Bit-Level Multiplexor
  multiplexor (mux), selector
    Control signal s
    Data signals a and b
    Output a when s=1, b when s=0
Bit MUX
b
s
a
out
out = (s&&a)||(!s&&b)
HCL Expression

## Slide 8: Word Multiplexor
  Select input word A or B depending on control signal s
Word-Level Representation
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 9
Input a,b enables one of 4 outputs
  a,b = 00 -> out0
  a,b = 01 -> out1
  a,b = 10 -> out2
  a,b = 11 -> out3
a
b
Out0
Out1
Out2
Out3
Decoder

## Slide 10
a
b
Carry-out
Carry-in
sum
1-bit Adder: Properties
  Fill out a Truth Table
  Write out Boolean Expressions for outputs
    S = (a’⋅b’⋅Cin) + (a’⋅b⋅Cin’) + (a⋅b’⋅Cin’) + (a⋅b⋅Cin)
    Cout =(b ⋅ Cin) + (a ⋅ Cin) + (a⋅b)
  Simplify expressions, if possible
  a b Cin S Cout
  0 0 0 0 0
  0 0 1 1 0
  0 1 0 1 0
  0 1 1 0 1
  0 0 1 0
  1 0 1 0 1
  1 1 0 0 1
  1 1 1 1 1
1-bit Adder

## Slide 11
  Carry-Out implementation
  Cout =(b ⋅ Cin) + (a ⋅ Cin) + (a⋅b)
  Similar implementation of Sum (quiz)

## Slide 12
1-bit ALU
  1-bit ALU
    1-bit adder
    Logical unit: and/or

## Slide 13
1-bit ALU
  Capable of
  ADD, AND, and OR
  How to add SUB ?
    -b = ~b + 1
    a – b = a + (b’ + 1)
    Add Binvert
    How to add 1 ?

## Slide 14
1-bit ALU (Full)
  ADD, AND, OR, SUB
  How to add NOR ?
    (A+B)’ = A’B’

## Slide 15
CarryIn
ALU0
CarryOut
CarryIn
Operation
a0
b0
Result0
CarryIn
ALU1
CarryOut
a1
b1
Result1
CarryIn
ALU2
CarryOut
a2
b2
Result2
CarryIn
ALU 31
CarryOut
a31
b31
Result31



From 1-bit ALU to
32-bit ALU
  Chain carry-out to carry-in to the next bit
  Set CarryIn in the least significant bit to 1 for subtraction
32-bit ALU

## Slide 16
32-bit ALU
Comparison: a < b ?
  if a < b, then a-b < 0 => Check for SIGN bit after subtraction
  However, the result of subtraction is not of interest
  Needs only the sign bit and rest of bits of 0’s

## Slide 18
32-bit ALU (Full)
Comparison: a = b (beq) ?
  if a = b, then a-b = 0
  we subtract b from a, then test for all 0’s
  Need a zero detector
    Zero = 1 if all result bits are 0’s (couter-intuitive)
Subtraction: Add (b’ + 1)
  Use Bnegate = Binvert + CarryIn