## Slide 1
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
valA  R[rA]
valB  R[rB]
Decode
valE  valB OP valA
Set CC
Execute
Memory
R[rB]  valE
Write
back
PC  valP
PC update
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
valA  R[rA]
valB  R[rB]
valE  valB + valC
M8[valE]  valA
PC  valP
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
valA  R[%rsp]
valB  R[%rsp]
valE  valB + 8
valM  M8[valA]
R[%rsp]  valE
R[rA]  valM
PC  valP
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Cnd  Cond(CC,ifun)
PC  Cnd ? valC : valP

## Slide 2: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  icode, ifun: Generate no-op if invalid address
  Need regids: Does this instruction have a register byte?
  Need valC: Does this instruction have a constant word?
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 3: Decode Logic
Register File
  Read ports A, B
  Write ports E, M
  Addresses are register IDs or 15 (0xF) (no access)
Control Logic
  srcA, srcB: read port addresses
  dstE, dstM: write port addresses
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd
Signals
  Cnd: Indicate whether or not to perform conditional move
    Computed in Execute stage

## Slide 4: A Source
int srcA = [
icode in {IOPQ, IRRMOVQ, IRMMOVQ, IPUSHQ}: rA;
icode in {IPOPQ, IRET}: RRSP;
1 : RNONE; # Don't need register
];
cmovXX rA, rB
valA  R[rA]
Decode
Read operand A
rmmovq rA, D(rB)
valA  R[rA]
Decode
Read operand A
popq rA
valA  R[%rsp]
Decode
Read stack pointer
jXX Dest
Decode
No operand
call Dest
valA  R[%rsp]
Decode
Read stack pointer
ret
Decode
No operand
OPq rA, rB
valA  R[rA]
Decode
Read operand A

## Slide 5: E Desti- nation
int dstE = [
icode in {IRRMOVQ} && Cnd: rB;
icode in {IIRMOVQ, IOPQ} : rB;
icode in {IPUSHQ, IPOPQ, ICALL, IRET}: RRSP;
1 : RNONE; # Don't write any register
];
None
R[%rsp]  valE
Update stack pointer
None
R[rB]  valE
cmovXX rA, rB
Write-back
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Conditionally write back result
R[%rsp]  valE
Update stack pointer
R[%rsp]  valE
Update stack pointer
R[rB]  valE
OPq rA, rB
Write-back
Write back result

## Slide 6: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  cond
    Computes conditional jump/move flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?
CC
ALU
ALU
A
ALU
B
ALU
fun.
Cnd
icode
ifun
valC
valB
valA
valE
Set
CC
cond

## Slide 7: ALU A Input
int aluA = [
icode in {IRRMOVQ, IOPQ}: valA;
icode in {IIRMOVQ, IRMMOVQ, IMRMOVQ}: valC;
icode in {ICALL, IPUSHQ}: -8;
icode in {IRET, IPOPQ}: 8;
# Other instructions don't need ALU
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPq rA, rB
Execute

## Slide 8: ALU Oper- ation
int alufun = [
icode == IOPQ : ifun;
1 : ALUADD;
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovl rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute

## Slide 9: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  stat: What is instruction status?
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat

## Slide 10: Instruction Status
Control Logic
  stat: What is instruction status?
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat
## Determine instruction status
int Stat = [
imem_error || dmem_error : SADR;
!instr_valid: SINS;
icode == IHALT : SHLT;
1 : SAOK;
];

## Slide 11: Memory Address
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVQ, IPUSHQ, ICALL, IMRMOVQ } : valE;
icode in { IPOPQ, IRET } : valA;
# Other instructions don't need address
];

## Slide 12: Memory Read
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVQ, IPOPQ, IRET };

## Slide 13: PC Update Logic
New PC
  Select next value of PC
New
PC
Cnd
icode
valC
valP
valM
PC

## Slide 14: PC Update
OPq rA, rB
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Cnd ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Cnd : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 15: SEQ Operation
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 16: SEQ Operation #2
  state set according to second irmovq instruction
  combinational logic starting to react to state changes
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 17: SEQ Operation #3
  state set according to second irmovq instruction
  combinational logic generates results for addq instruction
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
0x016
000
%rbx
<--
0x300
Read
Write
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 18: SEQ Operation #4
  state set according to addq instruction
  combinational logic starting to react to state changes
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 19: SEQ Operation #5
  state set according to addq instruction
  combinational logic generates results for je instruction
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write

## Slide 20: SEQ Summary
Implementation
  Express every instruction as series of simple steps
  Follow same general flow for each instruction type
  Assemble registers, memories, predesigned combinational blocks
  Connect with control logic
Limitations
  Too slow to be practical
  In one cycle, must propagate through instruction memory, register file, ALU, and data memory
  Would need to run clock very slowly
  Hardware units only active for fraction of clock cycle