## Slide 1
2.1.1. Number System
Base b => Decimal (Value)
Decimal (Value) => Base b
Base b arithmetic
Characters

## Slide 2
Base b
  Use only digits of 0, 1, 2,…., b-1
  Positional weights
    X = an-1 bn-1 + an-2 bn-2 + …. + a0 b0
    123 = 1x102 + 2x101 + 3x100
    What are a2, a1, and a0 in
    123 = a2x82 + a1x81 + a0x80

## Slide 3
Number System
Fraction
    X.Y = an-1 bn-1 + an-2 bn-2 + …. + a0 b0 + a-1 b-1 + a-2 b-2 + …
    123.45 = a2x82 + a1x81 + a0x80 + a-1x8-1 + a-2x8-2 + …
    Separate whole number & fraction
    123 = a2x82 + a1x81 + a0x80
    0.45 = a-1x8-1 + a-2x8-2 + …

## Slide 4
Binary to Decimal
https://www.youtube.com/watch?v=TD6lcIIOeic
Multiply positional weights by digits and add
  1 1 1 1 0
  24 23 22 21 20
  Resulting decimal number represents the value

## Slide 5
Decimal to Binary
X = an-1 bn-1 + an-2 bn-2 + …. + a0 b0
Decimal number D to base-2 number X
  Continue dividing D by 2
  Take the last quotient and all remainder
  30 10 -> 11110 2
30
15 -- 0
7 -- 1 3 -- 1
1 -- 1

## Slide 6
Other Number System ?
base 12
base 16
base 60 ?
  http://en.wikipedia.org/wiki/Sexagesimal

## Slide 7
Bases 2, 8, 16, etc.
3 binary bits into a single octal
4 binary bits into a single hex
  11110 2
  36 8
  1E X
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as 0xFA1D37B
      Or 0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 8
Arithmetic in bases
base 10
  Addition – carry
  Subtraction -- borrow
base 16

## Slide 9
Digital World
  Why not decimal numbers in computers ?
    Difficult to store
      ENIAC (1st electronic computer) used 10 vacuum tubes
    Difficult to transmit
    Messy for digital logic functions
      Addition, multiplication, etc.

## Slide 10
Binary Representations
Shannon’s Information Theory
Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
  Straightforward implementation of arithmetic functions
0.0V
0.5V
2.8V
3.3V
0
1
0

## Slide 11
2.1.2-2.1.5 Memory Words
Numbers
  All in binaray – can be converted to octal, hex
Characters
  ASCII – 1-byte/char
  Unicode – 2-byte/char
    Unicode-table.com/en
    http://www.tamasoft.co.jp/en/general-info/unicode.html
Program codes

## Slide 12
Bytes vs. Words
Machine Has “Word Size”
  Byte – a basic unit of information storage
  Word – a unit accessed at one time
    Most current machines have 64-bit word (8 bytes)
    We limit to 32-bits (4 bytes) machines
    Machines support multiple data formats
      Fractions or multiples of word size
      Always integral number of bytes

## Slide 13
Data Representations
C Data Type | Typical 32-bit | Intel IA32 | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 4 | 8
long long | 8 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | 8 | 10/12 | 10/16
pointer | 4 | 4 | 8

## Slide 14
byte
8 bits
short
int
float
long
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
double
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
8 bits
char
8 bits
Sizes of Primitive Types

## Slide 15
Word-Oriented Memory Org.
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)

## Slide 16
Byte Ordering
How should bytes within multi-byte word be ordered in memory?
Conventions
  Sun’s, Mac’s are “Big Endian” machines
    Least significant byte has highest address
  Alphas, PC’s are “Little Endian” machines
    Least significant byte has lowest address
  Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 17
char S[6] = "15213";
Representing Strings
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Other encodings exist, but uncommon
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
    Data are single byte quantities
  Text files generally platform independent
    Except for different conventions of line termination character(s)!
Linux/Alpha S
Sun S
32
31
31
35
33
00
32
31
31
35
33
00

## Slide 18
Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * creates byte array
typedef unsigned char *pointer;
void show_bytes(pointer start, int len)
{
int i;
for (i = 0; i < len; i++)
printf("0x%p\t0x%.2x\n",
start+i, start[i]);
printf("\n");
}
printf directives:
  %p: Print pointer
  %x: Print Hexadecimal

## Slide 19
show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 15213;
0x11ffffcb8 0x6d
0x11ffffcb9 0x3b
0x11ffffcba 0x00
0x11ffffcbb 0x00
6D
3B
00
00
Linux/Alpha A
3B
6D
00
00
Sun A